## Slide 1
Vision-Based Smart Parking Occupancy Detection System
Using Dual YOLO Architecture
Group:
Group 66011049 · 66011666 · 66011117
Members:
Kunanon Rungsomboon · Mihini Methasa Boteju · Papangkorn Wongsuwan
Advisor:
Jirayut Petchhan
Course:
01276390 CEPP | April 2026
CEIPP | 2026

## Slide 2
2
Background — The Parking Problem
⏱
17 Minutes Lost
Average time per trip spent searching for a parking spot — causing congestion, fuel waste, and emissions
💰
Expensive Sensors
Per-bay magnetic loops / ultrasonic sensors: cost, wiring, and maintenance scale linearly with bay count
📐
Perspective Distortion
Single-model detectors fail: cars far from camera appear smaller, making fixed-distance matching unreliable
Solution: Vision-only system using Dual YOLO + Bird's Eye View occupancy matching — no per-bay hardware

## Slide 3
Current Methods & Limitations
Manual Monitoring
Security personnel conduct physical walkthroughs — not scalable, error-prone
Per-Bay Sensors
Magnetic / ultrasonic sensors per space — high cost, difficult to maintain
Single-Model Vision
One CNN for all tasks — lower accuracy, struggles with multi-class inference
Perspective Distortion
Far objects appear smaller; naïve pixel-distance matching fails
Manual Spot Annotation
Parking bay coordinates must be hand-labelled — labour intensive, brittle
3

## Slide 4
Key Insights
Four ideas that define our approach
01
One Camera, Many Slots
A single overhead camera can monitor an entire parking zone, eliminating per-bay sensor hardware.
02
Separate the Detection Tasks
Spot detection and car detection are different problems using dedicated models for each yield's higher accuracy.
03
BEV Fixes Perspective
Bird's Eye View projection normalises distance distortion, making proximity matching reliable across the entire lot.
04
Recalibration Reduces Maintenance
Automated 2 AM spot re-scan self-heals after camera drift, eliminating the need for human re-annotation.
4

## Slide 5
💻
MACHINE
Lenovo Laptop
Model 83DG · Windows 11 Home 64-bit
🎮
GPU
NVIDIA GeForce RTX 4060
Laptop GPU · 8 GB VRAM · CUDA-enabled
⚡
CPU
Intel Core i7-14650HX
24 CPUs · 2.2 GHz
🧠
RAM
16 GB
System Memory
🔧
FRAMEWORK
Ultralytics YOLO
CUDA Acceleration + PyTorch
5
Training Hardware
All training and inference benchmarking performed on a single laptop with CUDA acceleration

## Slide 6
System Overview
Reference Image
→
Spot Detector (spots.pt)
→
Spot Coordinates JSON
→
BEV Transform
→
Matching Algorithm
→
Occupancy Output
Live Video
→
Car Detector (best.pt) + Tracker
↑
★ Red boxes = YOLO model inference
6

## Slide 7
System Architecture — Vision-Based Smart Parking
Two-phase pipeline: Initialization (once at startup) + Main Processing Loop (every frame)
Video Input/Output
Spot Detection/BEV
Matching & Dashboard
NMS Filter
Config Files
INITIALIZATION PHASE
Reference
Image (.jpg)
spots.pt
Spot Detector
spots_data.json
37 bay coords
⟳ Auto-recalibrate at 2AM (≤2 cars)
Spot BEV coords
MAIN PROCESSING LOOP
(every frame)
NMS Filter
IoU>0.4 suppressed
config.yaml
thresholds · paths
homography.json
BEV calibration
CCTV / Live
Video Feed
Video Frame
per frame
best.pt
Vehicle Detector
+ Tracker
Bird's Eye
View
Perspective
Transform
Greedy BEV
Matching O(K log K)
70px threshold
Occupancy
Car ↔ Spot
Assignment
Dashboard
FREE/OCCUPIED
Overlay (OpenCV)
7
System Architecture

## Slide 8
Implementation & Tools
Python 3.8+
Core programming language
OpenCV 4.x
Video capture, BEV transform, visualisation
Ultralytics YOLOv11
Object detection & real-time tracking
NumPy
Numerical arrays & distance computation
PyYAML
Configuration file loading (config.yaml)
JSON stdlib
Persistent spot coordinate storage
Module Structure
src/main.py — Entry point & main loop
modules/detector/ — YOLOv11 car detector wrapper
modules/parking_logic/
/spot_manager.py — Spot detection, NMS, BEV matching
/perspective.py — Homography / BEV transform
src/visualization.py — OpenCV drawing utilities
config/config.yaml — Runtime settings
config/spots_data.json— 37 persisted spot coords
config/reference.jpg — Empty lot reference image
8
Roboflow
End to end computer vision web platform

## Slide 9
Core Technical Method
Dual YOLOv11 Models
• spots.pt — detects empty bay boundaries from a reference image
• best.pt — tracks vehicles frame-by-frame in live video
• Each model is specialized, smaller, and more accurate than a single multi-task model
Homography / Bird's Eye View
• 4 anchor points map camera view → flat top-down canvas (400 × 800 px)
• Car's tyre contact point & spot centre both projected to BEV
• Eliminates perspective-induced scale variation between near/far spots
Distance-Based Greedy Matching
• All (car, spot) BEV distance pairs computed each frame
• Sorted ascending — closest pairs assigned first (greedy, O(K log K))
• 70 px BEV threshold rejects implausible matches
Self-Healing Recalibration
• Simulated clock triggers spot re-scan at 2:00 AM
• Only fires when ≤ 2 cars detected (low traffic window)
• Re-saves spots_data.json — no human annotation required
9

## Slide 10
spots.pt — Spot Detector
Input
Clean reference image (config/reference.jpg)
Trigger
Once at startup; again at 2 AM self-heal
Task
Locate empty parking bay boundaries via YOLO
Output
37 bounding boxes → saved to spots_data.json
best.pt — Vehicle Detector (y11s ★)
Input
Every live video frame (real-time stream)
Trigger
Every frame continuously
Task
Detect and track vehicles with persist IDs
Output
BBox + confidence score + track ID per car
Two dedicated models > one unified model: each optimised for its task → higher accuracy, lower compute per frame
Dual-Model Architecture
10

## Slide 11
Dataset Collection & Annotation
KMITL Campus Security Camera — Parking Area
Video Source
KMITL CCTV (existing infrastructure)
Recording Period
12 Days
Time Windows / Day
4 (Morning · Afternoon · Evening · Night)
Frames / Window
50
Total Frames
2,400
Annotation Classes
Parking Spot & Vehicle / Car
Platform
Roboflow
Time-stratified sampling → training data covers full day/night lighting range
Dataset Collection & Annotation
11

## Slide 12
Bird's Eye View (BEV) Occupancy Matching
Camera view — perspective distortion visible
1
Homography Calibration
4 ground-plane anchor points → 3×3 matrix maps trapezoidal camera region to flat 400×800 px BEV canvas
2
BEV Projection
Car bottom-center (tyre contact point) and spot centers both transformed to scale-normalized BEV coordinates
3
Greedy Matching O(K log K)
All (car, spot) pairs scored by Euclidean distance in BEV. 70 px threshold filters implausible matches.
One fixed 70 px threshold works correctly across the entire lot — near and far from camera
12

## Slide 13
Bird's Eye View (BEV) Occupancy Matching
1
Homography Calibration
4 ground-plane anchor points → 3×3 matrix maps trapezoidal camera region to flat 400×800 px BEV canvas
13

## Slide 14
Bird's Eye View (BEV) Occupancy Matching
1
BEV Projection
Car bottom-center (tyre contact point) and spot centers both transformed to scale-normalized BEV coordinates
14

## Slide 15
Bird's Eye View (BEV) Occupancy Matching
1
Greedy Matching O(K log K)
All (car, spot) pairs scored by Euclidean distance in BEV. 70 px threshold filters implausible matches.
15

## Slide 16
Model Training
Training Configuration
Hyperparameter
Value
Epochs
50
Image Size
640 × 640 px
Batch Size
8
Optimizer
AdamW (auto)
IoU Threshold
0.7
Pre-trained
Yes — COCO weights
Conf Threshold
0.15 (inference)
Four Variants Trained
Model ID
Architecture
Dataset
Notes
y11n
YOLOv11 Nano
Standard dataset
Smallest / fastest
y11s
YOLOv11 Small
Standard dataset
★ SELECTED — best accuracy
y26n
YOLOv11 Nano
26-class dataset
Tests class breadth
y26s
YOLOv11 Small
26-class dataset
Comparison baseline
All models trained with identical hyperparameters for fair comparison.
16

## Slide 17
Training Convergence — y11s Model (50 Epochs)
17
Figure 1. Training & validation loss curves + key metrics for y11s across 50 epochs.
All loss components decrease monotonically — stable convergence, no overfitting. Validation closely tracks training.

## Slide 18
Precision-Recall & F1 Analysis — y11s
18
Figure 2. Precision-Recall Curve
Figure 3. F1-Confidence Curve
High area under PR curve confirms robustness across confidence thresholds · Peak F1 > 0.95 at confidence ≈ 0.4

## Slide 19
Confusion Matrix & Sample Validation Predictions
19
Figure 4. Normalised Confusion Matrix — y11s validation set
Figure 5. Sample validation batch predictions — y11s (high confidence, diverse scenes)
High on-diagonal values confirm reliable classification — minimal false positives and false negatives

## Slide 20
Figure 6. config/reference.jpg — spots.pt detected 37 parking bays at 2688×1520 px. Coordinates saved to spots_data.json.
37
Bays detected
2688×1520
Reference resolution
Once
Runs at startup only
2 AM
Auto-recalibration
JSON
Coordinates persisted
Parking Spot Detection — Reference Image Output
20

## Slide 21
Performance Results
Model
Precision
Recall
mAP@50
mAP@50-95
Train Time (s)
y11n (YOLOv11n, std)
0.961
0.923
95.7%
77.4%
5,597
y11s (YOLOv11s, std) ★
0.976
0.937
96.4%
80.7%
6,729
y26n (YOLOv11n, 26-cls)
0.928
0.905
95.1%
75.2%
5,448
y26s (YOLOv11s, 26-cls)
0.965
0.930
96.2%
80.8%
5,303
96.4%
mAP@50
80.7%
mAP@50-95
37
Spots Detected
y11s
Deployed Model
★ Selected for deployment
21
Model Comparison — Epoch 50 Results

## Slide 22
ONNX Speed & Efficiency
Model | CPU ONNX (ms) | GPU (ms) | Params (M) | FLOPs (B)
y11n | 30.35 | 26.89 | 2.59 | 3.22
y11s ★ | 58.13 | 10.89 | 9.43 | 10.77
y26n | 26.59 | 10.68 | 2.50 | 2.89
y26s | 54.60 | 11.16 | 9.95 | 11.25
Real-World Throughput (7,200 frames)
Model | FPS | Latency (ms) | Total (s)
y11n | 97.18 | 10.29 | 74.09
y11s ★ | 102.85 | 9.72 | 70.01
y26n | 101.97 | 9.81 | 70.61
y26s | 99.04 | 10.10 | 72.70
y11s wins on all metrics
mAP@50
96.4%
Highest accuracy
mAP@50-95
80.7%
Best generalization
Throughput
102.85 FPS
Fastest real-world
Latency
9.72 ms
Lowest per-frame
Note: larger y11s model achieves higher FPS than y11n — better GPU kernel alignment outweighs extra parameters
Real-World Performance Benchmarks
22

## Slide 23
System Behaviour — Demo Timeline
02:00 AM
Low Occupancy (≤ 2 cars)
Self-healing recalibration triggered. spots.pt re-scans live frame, updates spot registry & JSON.
09:30 AM
Medium Occupancy
Accurate FREE / TAKEN labels on all 37 spots. Dashboard reflects correct counts in real time.
16:00 PM
Peak Occupancy
HIGH occupancy correctly identified. Dashboard updates live as cars enter and occupy bays.
18:00 PM
Variable Occupancy
Smooth real-time transitions as vehicles enter and exit bays. Greedy matching resolves instantly.
23

## Slide 24
Current Progress & Limitations
Completed
• YOLOv11 model training (4 variants benchmarked)
• Parking spot detection — spots.pt, NMS, JSON persistence
• Bird's Eye View homography transform
• Greedy BEV distance-based occupancy matching
• Self-healing 2 AM recalibration mechanism
• Real-time dashboard overlay (OpenCV)
In Progress
• Demo video polishing & screen capture
• UI refinement — label styling, color overlays
Future Work
• Multi-camera orchestration
• IoT / MQTT cloud integration
• License plate recognition (ALPR)
• Edge deployment (Jetson / Coral TPU)
24

## Slide 25
Conclusion
What We Built
• Dual YOLOv11 pipeline: spots.pt (bay detection) + best.pt (vehicle tracking)
• Bird's Eye View perspective normalization eliminates camera distortion
• Greedy BEV matching assigns cars to spots in O(K log K) per frame
• Self-healing recalibration at 2 AM — zero manual re-annotation
• Deployed model (y11s): mAP@50 = 96.4%, mAP@50-95 = 80.7%
Why It Matters
High-accuracy real-time parking management with no per-bay hardware. Purely software-based — cost-effective, scalable, and maintainable.
Next Steps
→ Multi-camera facility-wide coverage
→ IoT / MQTT real-time data streaming
→ Mobile app driver notifications
→ ALPR for permit enforcement
→ Edge deployment (Jetson / Coral TPU)
→ Adaptive BEV threshold learning
Thank You | Q & A
25